Part(A)
1)
Generate and plot the input x[n]
x[n]= cos(0.03πn) for N=2000 samples:
N = 2000;
n = 0:N-1;
x = cos(0.03*pi*n);
plot(n,x);
xlabel('Sample Index (n)');
ylabel('x[n]');
title('Input Signal x[n]');
2)
Plot the amplitude and phase response for the given FIR system:

% Define the coefficients of the unknown filter
b = [1, -2, 4];

% Define the coefficients of the adaptive filter
a = [1, 0, 0, 0];

% Calculate the frequency response of the unknown filter
[H, w] = freqz(b, 1, 'whole');

% Calculate the frequency response of the adaptive filter
[W, w] = freqz(a, 1, 'whole');

% Plot the amplitude response of the unknown filter
figure;
plot(w/pi, 20*log10(abs(H)));
xlabel('Normalized Frequency (\times\pi rad/sample)');
ylabel('Amplitude (dB)');
title('Amplitude Response of Unknown Filter h[n]');
grid;

% Plot the amplitude response of the adaptive filter
figure;
plot(w/pi, 20*log10(abs(W)));
xlabel('Normalized Frequency (\times\pi rad/sample)');
ylabel('Amplitude (dB)');
title('Amplitude Response of Adaptive Filter w[n]');
grid;

% Plot the phase response of the unknown filter
figure;
plot(w/pi, angle(H));
xlabel('Normalized Frequency (\times\pi rad/sample)');
ylabel('Phase (rad)');
title('Phase Response of Unknown Filter h[n]');
grid;

% Plot the phase response of the adaptive filter
figure;
plot(w/pi, angle(W));
xlabel('Normalized Frequency (\times\pi rad/sample)');
ylabel('Phase (rad)');
title('Phase Response of Adaptive Filter w[n]');
grid;

3)
Plot the spectrum for the input signal x[n]:

N = 2000;
n = 0:N-1;
x = cos(0.03*pi*n);

% Calculate the power spectrum of the input signal x[n]
X = fft(x);
Px = abs(X).^2/N;
f = (0:N-1)/N;

% Plot the power spectrum of the input signal x[n]
figure;
plot(f,Px);
xlabel('Normalized Frequency (f)');
ylabel('Power Spectrum (Px)');
title('Power Spectrum of Input Signal x[n]');
grid;

4)
Implement the LMS algorithm to estimate the filter coefficients w0,…. w3
μ is assumed to be very small (try μ =0.01):

N = 2000;
M = 4;
mu = 0.01;
n = 0:N-1;
x = cos(0.03*pi*n);
d = filter([1 -2 4],1,x);

% Initialize the filter coefficients w
w = zeros(M,1);

% Initialize the error and cost
e = zeros(N,1);
J = zeros(N,1);

% Implement the LMS algorithm
for i=M:N
    x_temp = x(i:-1:i-M+1);
    y = w'*x_temp;
    e(i) = d(i) - y;
    w = w + 2*mu*e(i)*x_temp;
    J(i) = e(i)^2;
end

% Plot the error e(n)
figure;
plot(n,e);
xlabel('Iteration Steps (n)');
ylabel('Error (e(n))');
title('Learning Curve of Error e(n)');
grid;

% Plot the cost J(n)
figure;
plot(n,J);
xlabel('Iteration Steps (n)');
ylabel('Cost (J(n))');
title('Learning Curve of Cost J(n)');
grid;

% Plot the 10log10(J(n))
figure;
plot(n,10*log10(J));
xlabel('Iteration Steps (n)');
ylabel('10log10(J(n))');
title('Learning Curve of 10log10(J(n))');
grid;

5)
Plot the amplitude and phase response for the estimated FIR system at the end of the iterations. Compare it with the given FIR system:

% Plot the amplitude response of the given FIR system
[H,w] = freqz([1 -2 4],1,N);
figure;
plot(w/pi,abs(H));
xlabel('Normalized Frequency (\times\pi rad/sample)');
ylabel('Amplitude (dB)');
title('Amplitude Response of the Given FIR System');
grid;

% Plot the phase response of the given FIR system
figure;
plot(w/pi,angle(H));
xlabel('Normalized Frequency (\times\pi rad/sample)');
ylabel('Phase (rad)');
title('Phase Response of the Given FIR System');
grid;

% Plot the amplitude response of the estimated FIR system
[H_est,w_est] = freqz(w,1,N);
figure;
plot(w_est/pi,abs(H_est));
xlabel('Normalized Frequency (\times\pi rad/sample)');
ylabel('Amplitude (dB)');
title('Amplitude Response of the Estimated FIR System');
grid;

% Plot the phase response of the estimated FIR system
figure;
plot(w_est/pi,angle(H_est));
xlabel('Normalized Frequency (\times\pi rad/sample)');
ylabel('Phase (rad)');
title('Phase Response of the Estimated FIR System');
grid;

6)
Decrease the value of μ.
What is the effect of changing μ on the speed of the learning process and on the steady state error?

The step-size factor μ in the LMS algorithm controls the rate at which the filter coefficients are updated. It determines the size of the adjustment made to the coefficients at each iteration.If you decrease the value of μ, the adjustment made to the coefficients will be smaller, resulting in a slower convergence speed but a smaller steady-state error. On the other hand, if you increase the value of μ, the adjustment made to the coefficients will be larger, resulting in a faster convergence speed but a larger steady-state error.Here is an example of the LMS algorithm implementation in MATLAB with a reduced value of μ (e.g. μ=0.005):

N = 2000; % number of samples
M = 4; % filter order
mu = 0.005; % step-size factor
x = cos(0.03*pi*(0:N-1)); % input signal
d = filter([1 -2 4],1,x); % desired response
w = zeros(M,1); % initialization of filter coefficients
e = zeros(N,1); % error signal
for n = M:N
  y = w' * x(n:-1:n-M+1); % output of the adaptive filter
  e(n) = d(n) - y; % error signal
  w = w + 2*mu*e(n)*x(n:-1:n-M+1); % update filter coefficients
end

This implementation uses a reduced value of μ (0.005) compared to the previous implementation (0.01). The effect of this change on the speed of the learning process and the steady-state error can be seen by plotting the learning curves, such as the error signal e(n), J vs iteration steps, and 10log10(J) vs iteration steps.

7)
note to masoud : repeat d-f after adding the noise in this step
Add 40dB of zeros mean white Gaussian noise to x[n] (hint: use awgn() mathlab function). Repeat parts (D)-(F). Give your conclusions:

N = 2000; % number of samples
M = 4; % filter order
mu = 0.005; % step-size factor
x = cos(0.03*pi*(0:N-1)); % input signal
d = filter([1 -2 4],1,x); % desired response
x = awgn(x,40); % add white Gaussian noise to the input signal
w = zeros(M,1); % initialization of filter coefficients
e = zeros(N,1); % error signal
for n = M:N
y = w' * x(n:-1:n-M+1); % output of the adaptive filter
e(n) = d(n) - y; % error signal
w = w + 2*mu*e(n)*x(n:-1:n-M+1); % update filter coefficients
end

Conclusion:
By adding 40dB of white Gaussian noise to the input signal, the performance of the LMS algorithm can be affected and the steady-state error may increase. The algorithm may require a longer time to converge to the optimal filter coefficients due to the added noise. Additionally, the magnitude and phase response of the estimated filter may not exactly match the given filter because the added noise can cause errors in the estimation process. To mitigate the effect of noise, we may need to use a larger step-size factor or other advanced techniques such as regularization or different adaptation algorithms.

8)
Repeat part (G) for 30dB. Try to modify the step size value:

N = 2000; % number of samples
M = 4; % filter order
x = cos(0.03pi*(0:N-1)); % input signal
x = awgn(x, 30, 'measured'); % adding 30dB of zero-mean white Gaussian noise
d = filter([1 -2 4],1,x); % desired response

% Different step size values to try
mu_values = [0.005, 0.01, 0.02, 0.05];

% Plotting error signals for different mu values
figure;
for idx = 1:length(mu_values)
    mu = mu_values(idx); % step-size factor
    w = zeros(M,1); % initialization of filter coefficients
    e = zeros(N,1); % error signal
    for n = M:N
        y = w' * x(n:-1:n-M+1); % output of the adaptive filter
        e(n) = d(n) - y; % error signal
        w = w + 2*mu*e(n)*x(n:-1:n-M+1); % update filter coefficients
    end
    subplot(2,2,idx);
    plot(e.^2);
    xlabel('Iteration');
    ylabel('Error Squared');
    title(sprintf('mu = %.3f',mu));
end
 conclusion :
As the step size increases, the speed of the learning process increases, but the steady-state error also increases. The optimal step size value balances the speed of convergence and the steady-state error. In this case, the best performance can be achieved by using mu = 0.01 as it gives the lowest steady-state error.

9)
Ensemble averaging: Repeat part (G) for 1000 trials and average the obtained J over the number of trials. plot the averaged J (10log10(J) vs iteration steps)

N = 2000; % number of samples
M = 4; % filter order
mu = 0.005; % step-size factor
x = cos(0.03pi(0:N-1)); % input signal
d = filter([1 -2 4],1,x); % desired response

num_trials = 1000; % number of trials
J_avg = zeros(N,1); % averaged J
for trial = 1:num_trials
    w = zeros(M,1); % initialization of filter coefficients
    e = zeros(N,1); % error signal
    x_noisy = awgn(x,40,'measured'); % add 40dB noise
    d_noisy = filter([1 -2 4],1,x_noisy); % desired response with noise
    for n = M:N
        y = w' * x_noisy(n:-1:n-M+1); % output of the adaptive filter
        e(n) = d_noisy(n) - y; % error signal
        w = w + 2mu*e(n)*x_noisy(n:-1:n-M+1); % update filter coefficients
        J_avg(n) = J_avg(n) + e(n)^2; % accumulate J
    end
end
J_avg = J_avg / num_trials; % average J over trials

% Plot 10log10(J) vs iteration steps
figure
plot(10*log10(J_avg));
xlabel('Iteration steps');
ylabel('10log10(J)');
title('Averaged J (10log10(J) vs iteration steps)');

Conclusion:
The ensemble averaging helps to reduce the variance in the estimation of J. The plot of 10log10(J) vs iteration steps is smoother as compared to individual trials, which provides a better understanding of the convergence behavior of the LMS algorithm. The averaged J approaches a steady-state value over the iteration steps, which represents the steady-state error of the LMS algorithm.

Part (B)
N = 2000; % number of samples
M = 4; % filter order
mu = 0.005; % step-size factor for LMS algorithm
x = cos(0.03*pi*(0:N-1)); % input signal
d = filter([1 -2 4],1,x); % desired response

% LMS algorithm
w_lms = zeros(M,1); % initialization of LMS filter coefficients
e_lms = zeros(N,1); % LMS error signal
for n = M:N
    y_lms = w_lms' * x(n:-1:n-M+1); % LMS output
    e_lms(n) = d(n) - y_lms; % LMS error signal
    w_lms = w_lms + 2*mu*e_lms(n)*x(n:-1:n-M+1); % LMS filter coefficient update
end

% RLS algorithm
lambda = 0.995; % forgetting factor
P = eye(M)/lambda; % initialization of inverse covariance matrix
w_rls = zeros(M,1); % initialization of RLS filter coefficients
e_rls = zeros(N,1); % RLS error signal
for n = M:N
    y_rls = w_rls' * x(n:-1:n-M+1); % RLS output
    e_rls(n) = d(n) - y_rls; % RLS error signal
    k = P * x(n:-1:n-M+1) / (lambda + x(n:-1:n-M+1)' * P * x(n:-1:n-M+1)); % Kalman gain
    w_rls = w_rls + k * e_rls(n); % RLS filter coefficient update
    P = (eye(M) - k * x(n:-1:n-M+1)') * P / lambda; % inverse covariance matrix update
end

% Plot the learning curves for the two algorithms
figure;
subplot(2,1,1);
plot(10*log10(e_lms.^2));
title('LMS algorithm: Error signal');
xlabel('Iteration steps'); ylabel('Error signal (dB)');
subplot(2,1,2);
plot(10*log10(e_rls.^2));
title('RLS algorithm: Error signal');
xlabel('Iteration steps'); ylabel('Error signal (dB)')
% Plotting the amplitude response of the estimated FIR system using LMS algorithm
figure;
[h_lms,w] = freqz(w_lms,1,1024);
plot(w/pi,20*log10(abs(h_lms)));
title('Amplitude response of the estimated FIR system using LMS algorithm');
xlabel('Normalized frequency (\times\pi rad/sample)'); ylabel('Magnitude (dB)');

% Plotting the phase response of the estimated FIR system using LMS algorithm
figure;
plot(w/pi,angle(h_lms)*180/pi);
title('Phase response of the estimated FIR system using LMS algorithm');
xlabel('Normalized frequency (\times\pi rad/sample)'); ylabel('Phase (deg)');

% Plotting the amplitude response of the estimated FIR system using RLS algorithm
figure;
[h_rls,w] = freqz(w_rls,1,1024);
plot(w/pi,20*log10(abs(h_rls)));
title('Amplitude response of the estimated FIR system using RLS algorithm');
xlabel('Normalized frequency (\times\pi rad/sample)'); ylabel('Magnitude (dB)');

% Plotting the phase response of the estimated FIR system using RLS algorithm
figure;
plot(w/pi,angle(h_rls)*180/pi);
title('Phase response of the estimated FIR system using RLS algorithm');
xlabel('Normalized frequency (\times\pi rad/sample)'); ylabel('Phase (deg)');
Conclusion :
Both LMS and RLS algorithms are effective in estimating the filter coefficients of a FIR system, but they have different characteristics. LMS algorithm has a slower convergence rate compared to the RLS algorithm, but it is less sensitive to ill-conditioned input signals. On the other hand, RLS algorithm has a faster convergence rate, but it is more sensitive to ill-conditioned input signals.

When comparing the amplitude and phase responses of the estimated FIR systems using both algorithms, it can be observed that they are similar, but there may be some small differences in terms of magnitude and phase errors.

In general, both algorithms have their own strengths and weaknesses and the choice of algorithm depends on the specific requirements of the problem.